## Slide 1
Memory Organization 1 Lecture 40
Overview
Memory Hierarchy
Main Memory
Auxiliary Memory
Associative Memory
Cache Memory
Virtual Memory

## Slide 2
Memory Organization 2 Lecture 40
Memory Hierarchy
Magnetic
tapes
Magnetic
disks
I/O
processor
CPU
Main
memory
Cache
memory
Register
Cache
Main Memory
Magnetic Disk
Magnetic Tape
Memory Hierarchy is to obtain the highest possible access speed while minimizing the total cost of the memory system

## Slide 3
Memory Organization 3 Lecture 40
Main Memory
RAM and ROM Chips
Typical RAM chip
Typical ROM chip
Chip select 1
Chip select 2
Read
Write
7-bit address
CS1
CS2
RD
WR
AD 7
128 x 8
RAM
8-bit data bus
CS1 CS2 RD WR
0 0 x x
0 1 x x
1 0 0 0
1 0 0 1
1 0 1 x
1 1 x x
Memory function
Inhibit
Inhibit
Inhibit
Write
Read
Inhibit
State of data bus
High-impedence
High-impedence
High-impedence
Input data to RAM
Output data from RAM
High-impedence
Chip select 1
Chip select 2
9-bit address
CS1
CS2
AD 9
512 x 8
ROM
8-bit data bus

## Slide 4
Memory Organization 4 Lecture 40
Memory Address Map
Address space assignment to each memory chip
Example: 512 bytes RAM and 512 bytes ROM
RAM 1
RAM 2
RAM 3
RAM 4
ROM
0000 - 007F
0080 - 00FF
0100 - 017F
0180 - 01FF
0200 - 03FF
Component
Hexa
address
0 0 0 x x x x x x x
0 0 1 x x x x x x x
0 1 0 x x x x x x x
0 1 1 x x x x x x x
1 x x x x x x x x x
10 9 8 7 6 5 4 3 2 1
Address bus
Memory Connection to CPU
RAM and ROM chips are connected to a CPU through the data and address buses
- The low-order lines in the address bus select the byte within the chips and other lines in the address bus select a particular chip through its chip select inputs

## Slide 5
Memory Organization 5 Lecture 40
Connection of Memory to CPU
CS1
CS2
RD
WR
AD7
128 x 8
RAM 1
CS1
CS2
RD
WR
AD7
128 x 8
RAM 2
CS1
CS2
RD
WR
AD7
128 x 8
RAM 3
CS1
CS2
RD
WR
AD7
128 x 8
RAM 4
Decoder
3
2
1
0
WR
RD
9
8
7-1
10
16-11
Address bus
Data bus
CPU
CS1
CS2
512 x 8
ROM
AD9
1- 7
9
8
Data
Data
Data
Data
Data

## Slide 6
Memory Organization 6 Lecture 41
Auxiliary Memory
Information Organization on Magnetic Tapes
EOF
IRG
block 1 block 2
block 3
block 1
block 2
block 3
R1
R2 R3 R4
R5
R6
R1
R3 R2
R5 R4
file i
EOF
Organization of Disk Hardware
Track
Moving Head Disk Fixed Head Disk

## Slide 7
Memory Organization 7 Lecture 41
Associative Memory
Argument register(A)
Key register (K)
Associative memory
array and logic
m words
n bits per word
Match
register
Input
Read
Write
M
- Accessed by the content of the data rather than by an address
- Also called Content Addressable Memory (CAM)
Hardware Organization

## Slide 8
Memory Organization 8 Lecture 41
Organization of CAM
Internal organization of a typical cell Cij
C11
Word 1
Word i
Word m
Bit 1
Bit j
Bit n
M1
Mi
Mm
Aj
R
S
Output
Match
logic
Input
Write
Read
Kj
M
i
To
F
ij
K1
Kj
Kn
C1j
C1n
Ci1
Cij
Cin
Cm1
Cmj
Cmn
A1
Aj
An
i= word
j-= bit in word

## Slide 9
Memory Organization 9 Lecture 41
Match Logic
F'
i1
F
i1
K
1
A
1
F'
i2
F
i2
K
2
A
2
F'
in
F
in
K
n
A
n
. . . .
M
i

## Slide 10
Memory Organization 10 Lecture 42
Cache Memory
Locality of Reference
- The references to memory at any given time interval tend to be confined within a localized areas
- This area contains a set of information and the membership changes gradually as time goes by
- Temporal Locality
The information which will be used in near future is likely to be in use already( e.g. Reuse of information in loops)
- Spatial Locality
If a word is accessed, adjacent(near) words are likely accessed soon
(e.g. Related data items (arrays) are usually stored together;
instructions are executed sequentially)
Cache
- The property of Locality of Reference makes the cache memory systems work
- Cache is a fast small capacity memory that should hold those information
which are most likely to be accessed
Main memory
Cache memory
CPU

## Slide 11
Memory Organization 11 Lecture 42
Performance of Cache
All the memory accesses are directed first to Cache
If the word is in Cache; Access cache to provide it to CPU
If the word is not in Cache; Bring a block (or a line) including
that word to replace a block now in Cache
- How can we know if the word that is required is there ?
- If a new block is to replace one of the old blocks, which one should we choose ?
Memory Access
Performance of Cache Memory System
Hit Ratio - % of memory accesses satisfied by Cache memory system
Te: Effective memory access time in Cache memory system
Tc: Cache access time
Tm: Main memory access time
Te = Tc + (1 - h) Tm
Example: Tc = 0.4 s, Tm = 1.2s, h = 0.85%
Te = 0.4 + (1 - 0.85) * 1.2 = 0.58s

## Slide 12
Memory Organization 12 Lecture 42
Memory and Cache Mapping – (Associative Mapping)
Associative mapping
Direct mapping
Set-associative mapping
Associative Mapping
Mapping Function
Specification of correspondence between main memory blocks and cache blocks
- Any block location in Cache can store any block in memory
-> Most flexible
- Mapping Table is implemented in an associative memory
-> Fast, very Expensive
- Mapping Table
Stores both address and the content of the memory word
address (15 bits)
Argument register
Address
Data
0 1 0 0 0
0 2 7 7 7
2 2 2 3 5
3 4 5 0
6 7 1 0
1 2 3 4
CAM

## Slide 13
Memory Organization 13 Lecture 42
Cache Mapping – direct mapping
- Each memory block has only one place to load in Cache
- Mapping Table is made of RAM instead of CAM
- n-bit memory address consists of 2 parts; k bits of Index field and n-k bits of Tag field
- n-bit addresses are used to access main memory and k-bit Index is used to access the Cache
Addressing Relationships
Direct Mapping Cache Organization
Memory
address
Memory data
00000
1 2 2 0
00777
01000
01777
02000
02777
2 3 4 0
3 4 5 0
4 5 6 0
5 6 7 0
6 7 1 0
Index
address
Tag
Data
000
0 0
1 2 2 0
0 2
6 7 1 0
777
Cache memory
Tag(6) Index(9)
32K x 12
Main memory
Address = 15 bits
Data = 12 bits
512 x 12
Cache memory
Address = 9 bits
Data = 12 bits
00 000
77 777
000
777
n -k
k

## Slide 14
Addressing Relationships
Direct Mapping Cache Organization
Memory
address
Memory data
00000
1 2 2 0
00777
01000
01777
02000
02777
2 3 4 0
3 4 5 0
4 5 6 0
5 6 7 0
6 7 1 0
Index
address
Tag
Data
000
0 0
1 2 2 0
0 2
6 7 1 0
777
Cache memory
Tag(6) Index(9)
32K x 12
Main memory
Address = 15 bits
Data = 12 bits
512 x 12
Cache memory
Address = 9 bits
Data = 12 bits
00 000
77 777
000
777

## Slide 15
Memory Organization 15 Lecture 42
Cache Mapping – direct mapping
Operation
- CPU generates a memory request with (TAG;INDEX)
- Access Cache using INDEX ; (tag; data)
Compare TAG and tag
- If matches -> Hit
Provide Cache(data) to CPU
- If not match -> Miss
Search main memory and replace the block from cache memory
Direct Mapping with block size of 8 words
000
0 1
3 4 5 0
007
0 1
6 5 7 8
010
017
770
0 2
777
0 2
6 7 1 0
Block 0
Block 1
Block 63
Tag Block Word
INDEX

## Slide 16
Memory Organization 16 Lecture 42
Cache Mapping – Set Associative Mapping
Set Associative Mapping Cache with set size of two
- Each memory block has a set of locations in the Cache to load
Index
Tag
Data
000
0 1
3 4 5 0
0 2
5 6 7 0
Tag
Data
777
0 2
6 7 1 0
0 0
2 3 4 0

## Slide 17
Memory Organization 17 Lecture 42
Cache Write
Write Through
When writing into memory
If Hit, both Cache and memory is written in parallel
If Miss, Memory is written
For a read miss, missing block may be overloaded onto a cache block
Memory is always updated
-> Important when CPU and DMA I/O are both executing
Slow, due to the memory access time
Write-Back (Copy-Back)
When writing into memory
If Hit, only Cache is written
If Miss, missing block is brought to Cache and write into Cache
For a read miss, candidate block must be written back to the memory
Memory is not up-to-date, i.e., the same item in
Cache and memory may have different value

## Slide 18
Memory Organization 18 Lecture 43
Virtual Memory
Give the programmer the illusion that the system has a very large memory, even though the computer actually has a relatively small main memory
Address Space(Logical) and Memory Space(Physical)
Address Mapping
Memory Mapping Table for Virtual Address -> Physical Address
virtual address
(logical address)
physical address
address space
memory space
address generated by programs actual main memory address
Mapping
Virtual address
Virtual
address
register
Memory
mapping
table
Memory table
buffer register
Main memory
address
register
Main
memory
Main memory
buffer register
Physical
Address

## Slide 19
Memory Organization 19 Lecture 43
Address Mapping
Organization of memory Mapping Table in a paged system
Address Space and Memory Space are each divided into fixed size group of words called blocks or pages
1K words group
Page 0
Page 1
Page 2
Page 3
Page 4
Page 5
Page 6
Page 7
Block 3
Block 2
Block 1
Block 0
Address space
N = 8K = 213
Memory space
M = 4K = 212
0
000
1
001
1
010
0
011
0
100
1
101
1
110
0
111
1
Block 0
Block 1
Block 2
Block 3
MBR
0 1
0 1 0 1 0 1 0 0 1 1
1 0 1
0 1 0 1 0 1 0 0 1 1
Table
address
Presence
bit
Page no.
Line number
Virtual address
Main memory
address register
Memory page table
Main memory
11
00
01
10
01

## Slide 20
Memory Organization 20 Lecture 43
Associative Memory Page Table
Assume that
Number of Blocks in memory = m
Number of Pages in Virtual Address Space = n
Page Table
- Straight forward design -> n entry table in memory Inefficient storage space utilization
<- n-m entries of the table is empty
- More efficient method is m-entry Page Table
Page Table made of an Associative Memory
m words; (Page Number: Block Number)
1 0 1
Line number
Page no.
Argument register
1 0 1 0 0
0 0 1 1 1
0 1 0 0 0
1 0 1 0 1
1 1 0 1 0
Key register
Associative memory
Page no.
Block no.
Virtual address
Page Fault
Page number cannot be found in the Page Table

## Slide 21
Memory Organization 21 Lecture 43
Page Replacement
Modified page fault service routine
Decision on which page to displace to make room for
an incoming page when no free frame is available
  1. Find the location of the desired page on the backing store
  2. Find a free frame
  - If there is a free frame, use it
  - Otherwise, use a page-replacement algorithm to select a victim frame
  - Write the victim page to the backing store
  3. Read the desired page into the (newly) free frame
  4. Restart the user process
2
f
0
v
i
f
v
frame
valid/
invalid bit
page table
change to
invalid
4
reset page
table for
new page
victim
1
swap
out
victim
page
3
swap
desired
page in
backing store
physical memory

## Slide 22
Memory Organization 22 Lecture 43
Page Replacement Algorithms
FIFO
0
7
1
7
2
0
3
0
4
2
3
0
3
2
1
2
0
1
7
7
0
1
0
0
7
1
2
0
1
2
3
1
2
3
0
4
3
0
4
2
0
4
2
3
0
2
3
0
1
3
0
1
2
7
1
2
7
0
2
7
0
1
Page frames
Reference string
-
FIFO algorithm selects the page that has been in memory the longest time
Using a queue - every time a page is loaded, its
identification is inserted in the queue
Easy to implement
May result in a frequent page fault
0
7
1
7
2
0
3
0
4
2
3
0
3
2
1
2
0
1
7
0
1
0
0
7
1
2
0
1
2
0
3
2
4
3
2
0
3
2
0
1
7
0
1
Page frames

## Slide 23
Memory Organization 23 Lecture 43
Page Replacement Algorithms
- LRU uses the recent past as an approximation of near future.
Replace that page which has not been
used for the longest period of time
LRU
0
7
1
7
2
0
3
0
4
2
3
0
3
2
1
2
0
1
7
7
0
1
0
0
7
1
2
0
1
2
0
3
4
0
3
4
0
2
4
3
2
0
3
2
1
3
2
1
0
2
1
0
7
Page frames
Reference string
- LRU may require substantial hardware assistance
- The problem is to determine an order for the frames
defined by the time of last use